## Slide 1: Finding the Optimal Switch Box Topology for an FPGA Interconnect
Seyi Ayorinde
Pooja Paul Chaudhury

## Slide 2: FPGA
Field Programmable Gate Array
Reconfigurable Circuit
Configurable Logic Blocks (CLBs)
Calhoun et al.: Flexible Circuits and Architectures for Ultralow Power

## Slide 3: FPGA Interconnect
Wires
Connection Boxes (CBs)
Switch Boxes (SBs)
Calhoun et al.: Flexible Circuits and Architectures for Ultralow Power

## Slide 4: Why FPGAs?
Best of Both Worlds
Application-Specific Integrated Circuits (ASICs)
  Very Efficient, not very flexible
General Purpose Processors
  Very flexible, very inefficient
FPGAs
  Much more efficient than GPPs,
  Much more flexible than ASICs (reconfigurable)

## Slide 5: Interconnect – The Problem
Large source of Delay, Energy, and Area
  Parasitics in Interconnect – 25x-50x of an inverter
  60-70% of Power Dissipation
  75% of Area [1]
Multiple areas where interconnect can be optimized
  Wiring, Connection Boxes, Switch Boxes
Our goal:
Optimize Switch Box Topology

## Slide 6: Prior Work – Switch Box Topologies
Tri-state Inverter (TSI)

## Slide 7: Prior Work – Switch Box Topologies
Transmission Gate (TX) Pass Gate (PG)
Question: Which of these choices is best?

## Slide 8: High Performance vs. Low Energy
Pass Gates w/ Dual-VDD Implementation
Lower Delay in Sub- & Super-VT
  Better for High-Performance Applications
Transmission Gates
Lower Energy in Sub- and Super-VT
  Better for Low-Energy Applications

## Slide 9: Outline
Design Methodology
  Test Circuits
  Qualifications/Assumptions
Comparison of switches w/ Single VDD scheme
Comparison w/ Dual VDD scheme
Conclusions

## Slide 10: Test Circuit
Delay – after each Switch
Energy – Drawn from VDD
SWITCH-1
SWITCH-2
SWITCH-10
Inverter Load
INPUT SIGNAL

## Slide 11: Qualifications
Simplified Model of Interconnect
  Ideal Wiring
  No Leaky Off-path Branches
  Ideal Input Signal
  Simple Inverter Load
Other Possible Topologies
Delay measurement – 50%-50%
Energy Measurement – Idrawn x VDD x TSignal

## Slide 12: Signal Propagation in FPGA Interconnect
Pass Gate
Tri-State Inverter
Transmission Gate
Input Signal

## Slide 13: Signal Propagation in FPGA Interconnect
Not full
VDD Swing
Pass Gate

## Slide 14: Signal Propagation in FPGA Interconnect
Long Propagation Delay
Pass Gate

## Slide 15: Signal Propagation in FPGA Interconnect
Tri-State Inverter
Tri State Inverters – Good for High Performance Applications

## Slide 16: Current Draw in FPGA Interconnect
Switching Current

## Slide 17: Current Draw in FPGA Interconnect
Leakage & Static Current

## Slide 18: Current Draw in FPGA Interconnect
Pass Gate
Transmission Gate
Tri-State

## Slide 19: Current Draw in FPGA Interconnect
Transmission Gate
Transmission Gates – Good for Low Power Applications

## Slide 20: E-D Curves for Switches
Increasing VDD

## Slide 21: Why are PGs so bad?
PGs cannot pass good ‘1s’
  Lower Current during High Phase (increased Delay)
  Increased Static Current (increased Energy Drawn
If PGs could pull good 1’s:
  Comparable to TXs, but w/ less area (good)
Solution – Boost Gate Voltage of Pass Gate (VDDc)

## Slide 22: Effect of Changing VDDc - PGs
Increasing VDDc
VDD = 0.3V

## Slide 23: E-D Curves Revisited
Increasing VDD

## Slide 24: Current Drawn Revisited
Boosted Pass Gate
Pass Gate

## Slide 25: Current Drawn Revisited
Boosted Pass Gate
Pass Gate

## Slide 26: Conclusions
Pass Gates w/ Dual VDD Scheme – Good for High Performance
Transmission Gates – Good for Low Energy

## Slide 27: Further Study
Different Optimization of VDDc
  Minimize Static Current
Dual-VDD Schemes for other topologies
Other Switch Topologies
More intricate interconnect model
  Wire resistance and capacitance, non-ideal signals, etc.

## Slide 28: References
[1] Calhoun, B. H., J. Ryan, S. Khanna, M. Putic, and J. Lach, "Flexible Circuits and Architectures for Ultra Low Power", Proceedings of the IEEE, vol. 98, pp. 267-282, 02/2010.
[2] Ryan, J. F., and B. H. Calhoun, "A Sub-Threshold FPGA with Low-Swing Dual-VDD Interconnect in 90nm CMOS", Custom Integrated Circuits Conference (CICC), 20/09/2010.

## Slide 29: Thank you!